## Slide 1: Exceptions & Hardware support
TANZIR AHMED CSCE 313 Fall 2020
Reading Reference: Textbook 1 Chapter 2

## Slide 2: Altering the Control Flow
CPU executes instructions 1-at-a-time mostly sequentially
Program-assisted mechanisms for changing control flow:
  Jumps and branches—react to changes in program state
  Function call and return using stack discipline—react to program state
Insufficient for a useful system
  The user application is the central thing – how to let OS into the CPU unless the app gives up control?
  Thus, difficult for the CPU to react to other changes in system state
    Data arrives from a network adapter
    Instruction divides by zero
    User hits control-C at the keyboard
System needs mechanisms for “exception control flow”

## Slide 3: Exception Control Flow
An exception is a transfer of control to the OS in response to some event (i.e., change in processor state)
  It also gives “asynchronous” behavior
User Process
OS
exception
exception processing
by exception handler
exception
return (optional)
event
current
next

## Slide 4: Asynchronous Exceptions (Interrupts)
Caused by events external to processor (i.e., outside the current program)
  Indicated by setting the processor’s interrupt pin(s)
  Handler returns to “next” instruction after servicing
Examples:
  I/O interrupts
    Key pressed on the keyboard
    Arrival of packet from network, or disk
  Hard-reset interrupt
    Hitting reset button
  Soft-reset interrupt
    Hitting control-alt-delete to initiate restart on a PC

## Slide 5: Interrupt Vectors
  Each type of event has a unique exception number k
  Index into jump table (a.k.a., interrupt vector)
  Jump table entry k points to a function (exception handler).
  Handler k is called each time exception k occurs.
interrupt
vector
0
1
2
...
n-1
code for
exception handler 0
code for
exception handler 1
code for
exception handler 2
code for
exception handler n-1
...
Exception
numbers

## Slide 6: Synchronous Exceptions: Traps, Faults, Aborts
Caused as result of executing an instruction
  From within the CPU
3 types:
  System Calls
  Faults
  Aborts

## Slide 7: System Calls
Functions called by user programs to interact with the OS or request core OS services
However, unlike traditional functions, system calls must execute in some “privileged” mode so that has access to OS’s internal information and data structures etc.
  Hence, these are very different from regular function calls
  Example: Opening a File
  User calls open(filename, options)
  OS must find (if reading) or create (when writing) the file, consult permissions and get it ready
However, when everything checks out, it must also act like a regular function that returns a file descriptor
Let us see how a system call is implemented then
User Process
OS
exception
return
syscall

## Slide 8: Mechanism of System Calls
We need to take a closer look at the address space layout of program
The user stack maintains a collection of stack frames, but this is insecure for syscalls because someone could manipulate the SP and navigate all frames
  E.g., gdb can do that
Therefore, the solution to this is to keep OS’s internal data separately in a place calles kernel stack
The desired system call’s opcode is placed in reg %rax (e.g.,0 for read, 1 for write, 2 for open, 3 for close)
The CPU issues a software interrupt (aka, trap) , which invokes an interrupt handler executed in “privileged” mode
The interrupt handler makes a frame in Kernel Stack, places return value in %rax, then calls iretq (not retq) to return from the interrupt handler and revert to user mode
  %rax is then put in place of a return value
stack
Stack pointer (SP)
heap
data
code
shared libs
Addr=0
Addr=0xFFFFFFFFFFFFFFFF
Frame for main()
Frame for testfunc()
Frame for open()
Kernel stack

## Slide 9: Control Flow in System Calls
foo(){ open(“test”,“rw”);
}
User Program
open(arg1,arg2){ %rax=SYSOPEN(=2) trap copy %rax to stack retq }
User Stub
open_handler(arg1,arg2){ perform the actual file open operation …
}
Kernel
open_handler_stub(){ 1. Copy args from user memory 2. Validate args 3. callq open_handler(arg1,arg2) 4. put return value on %rax 5. iretq return
}
Kernel Stub
(1)
(6)
(2)
(5)
(3)
(4)
Dashed lines mean context switch due to software interrupt,
This is also where execution mode changes to/from “privileged”

## Slide 10: Faults
Attributes
  Unintentional but possibly recoverable
  Examples: Page Faults
  Either re-executes faulting (“current”) instruction or aborts
User Process
OS
Fault happened
Fault handled
Return to same instruction
event

## Slide 11: Fault Example #1
Memory Reference
  User writes to memory location
  That portion (page) of user’s memory is not mapped yet (because memory pages are mapped only when necessary)
  Page handler must load page into physical memory
  Returns to faulting instruction
  Successful on second try
User Process
OS
page fault
Allocate page and its mapping in page table
return
event
int a[1000];
main ()
{
a[500] = 13;
}

## Slide 12: Fault Example #2
Illegal Memory Reference
  User writes to memory location
  Address is not valid
  Page handler detects invalid address
  Sends SIGSEGV signal to user process
  User process exits with “segmentation fault”
int a[1000];
main ()
{
a[5000] = 13;
}
User Process
OS
page fault
Detect invalid address
event
Signal process

## Slide 13: Aborts
Attributes
  Unintentional and unrecoverable
  Examples: parity error, machine check, divide by zero
  Aborts current program or entire OS
  A way for the OS to put essential error checking

## Slide 14: Example: Web Server
syscall
wait
interrupt
RTU
syscall
wait
interrupt
RTU
syscall

## Slide 15: Summarizing Control Flow Exceptions
User programs are not in charge of (and therefore not burdened with) handling every exception
  Not every program will check for divide- by-0 error
Mechanism is used by OS to do things beyond error handling
  E.g., page faults are used to enable “lazy” physical memory allocation
Are Synchronous/Internal (Traps, Faults, Aborts) OR Asynchronous/External (I/O Interrupts, Hard or Soft Reset etc.)

## Slide 16: Architectural Support for OS
Operating systems mediate between applications and the physical hardware of the computer
However, a modern with all its features cannot run on a hardware that does not support it
  The hardware must be modified to accommodate OS

## Slide 17: Architectural Features
Protection Modes
  Protection Ring / 2 modes: User/kernel
  Privileged Instructions
Interrupts and Exceptions
System Calls
Timers (clock)
Memory Protection Mechanisms
I/O Control and Operation
Synchronization Primitives (e.g., atomic instructions)

## Slide 18: Dual-mode Execution
Every CPU has at least 2 modes of execution (the CPU alternates between the modes)
  Kernel-mode: Execution with the full privileges of the hardware
  User-mode: Execution with Limited privileges
    Only those granted by the operating system kernel
Allowed in both modes
Only allowed in Kernel mode
Full Instruction Set
In USER mode?
Perform necessary checks before executing
Execute (i.e., can do anything w/o checks)
yes
no
Any violation?
yes
Execute
no
Terminate program

## Slide 19: Privileged Instructions - Examples
Only the OS should be able to
  Directly access I/O devices (disks, printers..)
    Allows OS to enforce security and fairness
    User programs cannot possibly be fair to each other
  Manipulate memory management state
    E.g., page tables (Virtual-> Physical), protection bits, TLB entries, etc.
    Processes use them, but cannot modify – that would defeat the protection
  Adjust protected control registers
    User   Kernel modes or Raise/Lower interrupt level
  Execute CLF instruction
A small cache for page tables

## Slide 20: A Simple CPU Model – Needs Some Change
Select PC
Program Counter (PC)
CPU Instruction Fetch & Exec
+4
Opcode (if branch/jump)
branch/jump address
… 100: ADD $rs, $rt, $rd
104: JEQ $r1, $r2, -100 …

## Slide 21: A CPU with Dual-Mode Operation
Select PC
Program Counter (PC)
CPU Instruction Fetch & Exec
+4
branch/jump address
Mode
Select Mode
Exception/ Interrupt Handler PC
Opcode
If trap?
RTU?
None?
New PC
New Mode
Kernel
User
jump/branch?
Exception?
None?

## Slide 22: What are “Necessary” Checks?
One example: Kernel Memory Protection
Note that because of Virtual Memory, no process can harm another
  Then, why bother about memory protection?
However, the kernel is mapped into lower part of each process’s address space like in the picture:
Why is Kernel also included?
  To load and run the process in the first place
  Handle Interrupts, exceptions, and system calls
Therefore, kernel must be protected from a faulty or malicious user program
In USER mode?
Perform necessary checks before executing
Execute
yes
no
Any violation?
yes
Execute
no
Terminate program
Process
Kernel
Private address space

## Slide 23: Memory Protection
Could we just make Kernel memory read-only?
  No. Because kernel contain sensitive data that should not even be read
  Example: page tables
A primitive but effective solution in hardware:
  A Base and a Bound register for each process
  Cannot access (read or write) anything below base
This check is done only in User mode
  Kernel mode has unlimited access
Process
Kernel
Private address space
base
bound

## Slide 24: Hardware Timer
Operating system timer is a critical building block
  Many resources are time-shared; e.g., CPU
  Allows OS to prevent infinite loops
Fallback mechanism by which OS regains control
  When timer expires, generates an interrupt
  Handled by kernel, which controls resumption context
    Basis for OS scheduler; more later…
  Setting (and clearing) a timer is a privileged instruction

## Slide 25: Mode Switch
Mode separation does NOT mean that a user program cannot request a Kernel-mode operation
  User mode to kernel mode switch is very common
  How do we switch from one mode to the other?
    Such that the protection is not compromised

## Slide 26: User  Kernel Mode Switch
From user-mode to kernel-mode
  Interrupts
  (Synchronous) Exceptions (Faults and Aborts)
  System calls (traps) (aka protected procedure call)

## Slide 27: Kernel  User Mode Switch
From kernel-mode to user-mode
  New process/new thread start
    Jump to first instruction in program/thread
  Return from interrupt, exception, system call
    Resume suspended execution
  Process/thread context switch
    Resume some other process

## Slide 28: Safe Mode Transfer – Interrupt Handling
First, User->Kernel. The main idea is rather simple
  Store the state of the running process (so that it can be resumed later)
  Execute the handler
  Return to the interrupted process by restoring the saved state
But the actual implementation is a bit more complicated
We first need to know which process info must be stored
  Basically, the Process Control Block (PCB)

## Slide 29: Saving Process State: Difficulty
foo (){ x = x + 1; y = y - 2; }
User-level Process
CPU
PC=5000 SP EFLAGS Other Regs
User Stack
Handler (){ 100: save PC
104: … … }
Kernel
foo (){ 5000: x=x+1; 5004: y=y-2;
… }

## Slide 30: Saving Process State: Difficulty
foo (){ x = x + 1; y = y - 2; }
User-level Process
CPU
PC=100 SP EFLAGS Other Regs
User Stack
Handler (){ 100: save PC
104: … … }
Kernel
foo (){ 5000: x=x+1; 5004: y=y-2;
… }
Kernel Stack
This will only save 100, the PC of the handler. The original PC=5000 of user app is lost forever!!

## Slide 31: To Summarize
The processor has only 1 set of SP, PC, EFLAGS etc.
Any piece of code (e.g. handler code as well) will require its own PC (and also SP and others) first loaded into the CPU
Switching from User code to Handler code means overwriting PC, SP etc. with the handler PC, SP etc.
  But ALAS!!! We just lost the PC, SP for the user code
  How can we ever recover those??
Quoting the Anderson book: “This is akin to rebuilding the car’s transmission while it barrels down the road 60mph”
Solution: Take hardware help
  Clearly, any other code will also need PC, SP,..
  Hardware does not need to use SP, PC to implement a logic

## Slide 32: Plan of Action: Before Interrupt
foo (){ 5000:x=x+1; 5004:y=y-2; }
User-level Process
CPU
PC=5000 SP EFLAGS Other Regs
Registers
User Stack
handler (){ pushad
… }
Kernel
Kernel Interrupt Stack
Interrupts Enabled

## Slide 33: Plan of Action: Hardware Action
foo (){ 5000:x=x+1; 5004:y=y-2; }
User-level Process
CPU
PC SP EFLAGS Other Regs
Registers
User Stack
handler (){ pushad
… }
Kernel
Kernel Interrupt Stack
Interrupts Disabled
SP
PC(5000)
EFLAGS

## Slide 34: Plan of Action: As Handler Starts
foo (){ 5000:x=x+1; 5004:y=y-2; }
User-level Process
CPU
PC SP EFLAGS Other Regs
Registers
User Stack
handler (){ pushad
… }
Kernel
Kernel Interrupt Stack
Interrupts Disabled
SP
PC(5000)
EFLAGS
Other Regs

## Slide 35: User to Interrupt Handler – Mechanism on x86
Hardware does the following:
  Mask further interrupts
    they are stored, not thrown away
    Getting interrupted within handling an interrupt is problematic but possible
  Change mode to Kernel
  Copy PC, SP, EFLAGS to the Kernel Interrupt Stack (KIS)
  Change SP: to the KIS (above the stored PC, SP, EFLAGS)
  Change PC: Invoke the interrupt handler by vectoring through the Interrupt Vector Table (i.e., overwrite PC with the handler PC)
Software (i.e., the handler code) does the following:
  Stores the rest of the general-purpose registers being used by the interrupted process
  Does the rest of interrupt handling operation

## Slide 36: When Handler Ends
Software does the following:
  Handler code restores the saved general registers
Hardware does the following:
  Restores PC, SP, EFLAGS from Kernel Stack
  Reenable Interrupts
  Switch to user mode

## Slide 37: Sequential vs Nested Interrupt Handling
In x86, other interrupts are disabled to avoid confusion
  This keeps things simple, however, no levels of priority among interrupts
Therefore, many systems support nested interrupt handler
  Another interrupt handler will run if that is higher priority
  Can be implemented with a little bit of more complexity

## Slide 38: Summary: User/Kernel (Privileged) Mode
User Mode
Kernel Mode
Full HW access
Limited HW access
exec
syscall
exit
rtn
interrupt
rfi
FP exception
FP Exception error
Notes: Processor routinely checks for interrupts and if one is logged, it goes back to save the state of the process it is executing and enters the kernel to service the interrupt. The service is done by entering a interrupt vector table which contains the address of the specific interrupt service routine. Once the routine is serviced the kernel gives control back to the user process.
In multiprocessor systems, only one processor has to service the interrupt from an external device.
What happens when you move a mouse pointer? Each move or point or click registers as an interrupt which is noticed by the processor which moves the control back to the Kernel to service the interrupt routine and that shows up as an action to its associated process (e.g. move of mouse pointer in the active window, or highlight of a word selected, etc.)
An alternative to Interrupt would be “polling” where the Kernel would go in a round-robin fashion to check the status of each device to see if they have an interrupt.